## Slide 1: Multiresolution topology optimization Computational-efficiency assessment for the half MBB beam
Lukas Campaert · Tiebert Lefebure
Structural Optimization · B-KUL-H0T88A · Prof. M. Schevenels
Faculty of Engineering Science · Academic Year 2025-2026
Notes: PRESENTER: Lukas | Target ~20 s
Greeting. Our examination assignment is on multiresolution topology optimization, MTOP. In topology optimization the question is where to put material to make a structure as stiff as possible; here the question is whether we can answer that question faster. We assessed MTOP on the half MBB beam and compared it head-to-head with the classical approach. The image is our optimized beam.

## Slide 2: Problem statement and research question
Minimum-compliance topology optimization of the half MBB beam
MTOP (Nguyen et al., 2010): describe the design on a fine density mesh, solve the equilibrium on a coarser mesh
A smaller system K u = f should lower the computation time
The original paper reports no computation times or speedup factors
Research question: how large is the speedup, and is the optimized design preserved?
Structural Optimization (B-KUL-H0T88A)
2
Notes: PRESENTER: Lukas | Target ~50 s
Topology optimization distributes a fixed amount of material so the structure is as stiff as possible. The cost is dominated by repeatedly solving the finite element system K u = f.
MTOP, introduced by Nguyen and co-workers in 2010, splits the problem: the design is still described on a fine mesh, but the equilibrium equations are solved on a coarse mesh, which should be much cheaper.
The catch: the original paper never reported computation times. So our research question is exactly that - how large is the speedup, and does the optimized design stay the same?

## Slide 3: The structural model: half MBB beam
Half MBB beam, plane stress, bilinear Q4 elements
Unit point load at the upper-left corner
Symmetry support on the left edge, roller at the lower-right corner
Volume fraction 0.5, SIMP penalization power 3
Cone filter radius of 24 density cells
These settings are fixed for every experiment
Structural Optimization (B-KUL-H0T88A)
3
Notes: PRESENTER: Lukas | Target ~40 s
Our test structure is the half MBB beam from the Chapter 9 lecture code. A unit point load at the top-left corner, a symmetry condition on the left edge, and a roller at the bottom-right. Plane stress, bilinear quad elements.
The optimization targets a volume fraction of one half, SIMP penalization three, and a cone filter of radius 24 density cells. Important: these settings are identical for every experiment, so any difference we see is due to MTOP, not the parameters.

## Slide 4: The MTOP idea: decouple analysis from design
Classical: analysis mesh = density mesh (600 × 200)
MTOP: coarse 120 × 40 analysis mesh, 5 × 5 density cells per element
Same 600 × 200 design resolution, far fewer equations
Element stiffness by midpoint quadrature; 25 sub-cell templates precomputed once per run
Free degrees of freedom: 241,000 → 9,900
Structural Optimization (B-KUL-H0T88A)
4
Notes: PRESENTER: Lukas | Target ~70 s
This is the heart of MTOP. In the classical approach the analysis mesh and the design mesh are the same, 600 by 200.
In MTOP we keep the 600 by 200 design resolution, but we analyze on a coarse 120 by 40 mesh, with 5 by 5 density cells inside each finite element - that is the zoom on the right.
Each element's stiffness is integrated with one midpoint sample per density cell, so 25 small stiffness templates, which are precomputed once per run.
The payoff is the number of equations: the free degrees of freedom drop from about 241,000 to about 9,900. That factor is the speedup we are chasing.

## Slide 5: Optimization problem and experiment matrix
Design variables: the density of each density cell
Objective: minimize compliance (maximize stiffness)
Constraint: material volume fraction at most 0.5
SIMP material interpolation, penalization power 3
Cone filter, radius 24 cells (sensitivity or density)
Seven experiments: OC versus MMA, three filter / projection choices
Case | Approach | Optimizer | Filter / projection
1 | Classical | OC | Sensitivity filter
2 | MTOP | OC | Sensitivity filter
3 | Classical | OC | Density filter
4 | MTOP | OC | Density filter
5 | MTOP | MMA | Sensitivity filter
6 | MTOP | MMA | Density filter
7 | MTOP | MMA | Heaviside η = 0.3 / 0.5 / 0.7
Structural Optimization (B-KUL-H0T88A)
5
Notes: PRESENTER: Lukas | Target ~50 s
Quickly, the optimization problem. The design variables are the cell densities, the objective is to minimize compliance, and the constraint is the volume fraction of one half. SIMP with penalization three, and a cone filter of radius 24, used either as a sensitivity filter or a density filter.
We ran the seven experiments in the table: the optimality-criteria runs for assignment steps 1 to 3, then MMA for step 4 with sensitivity filtering, density filtering, and Heaviside projection at three thresholds. Every MTOP run has a classical counterpart for comparison.

## Slide 6: Verifying the implementation
Verified three derivative chains with three finite-difference strategies
Taylor remainder slope ≈ 2.00 confirms the analytical sensitivities
Structural Optimization (B-KUL-H0T88A)
6
Notes: PRESENTER: Lukas | Target ~40 s
Before trusting any result we verified the sensitivities - the gradients the optimizer relies on. We checked three derivative chains: the classical SIMP gradient, the MTOP per-cell gradient, and the full Heaviside chain, each with three finite-difference strategies.
The strongest is the Taylor remainder test, the right-hand panel: it should decay quadratically with the step size, and the fitted slope is essentially 2.00 for all three chains, with errors down to ten to the minus six. So the analytical gradients are correct.

## Slide 7: Steps 1 and 2: MTOP reproduces the classical design
Optimality criteria with sensitivity filtering
Same truss load path: top chord, bottom chord, triangulated web
Fine-mesh compliance: classical 224.6, MTOP 224.7 (+0.045 %)
Difference is a tiny boundary-level redistribution (RMS 0.003)
MTOP does not change the optimized design
Structural Optimization (B-KUL-H0T88A)
7
Notes: PRESENTER: Lukas | Target ~45 s
Now the results. Steps 1 and 2: optimality criteria with sensitivity filtering. On the right, the classical design on top, the MTOP design in the middle, and their difference at the bottom.
The two layouts are the same truss - a top chord, a bottom chord, a triangulated web. The difference plot is almost empty, just small boundary shifts, an RMS of three thousandths. Re-evaluated on the same fine mesh the compliances differ by 0.045 percent.
So MTOP does not change the design. I will hand over to Tiebert for how much faster it is.

## Slide 8: Steps 1 and 2: MTOP is 21× faster
Same convergence path: 94 versus 95 iterations
Wall-clock time: 263 s → 12 s
Speedup factor of 21 at matched compliance
The MTOP curve collapses against the time axis
Same design, same iterations, far less time
Structural Optimization (B-KUL-H0T88A)
8
Notes: PRESENTER: Tiebert (takes over from Lukas) | Target ~40 s
Thanks. So the designs are identical, but the timing is not. This plot is compliance against wall-clock time - classical in blue, MTOP in orange.
Both runs take essentially the same number of iterations, 94 and 95, so the optimization path is unchanged. But the classical run takes 263 seconds and the MTOP run takes 12 - a factor of 21. You can see the orange curve squeezed against the time axis.
Same design, same iteration count, 21 times faster.

## Slide 9: Step 3: density filtering
Same comparison with a density filter instead of a sensitivity filter
Designs again almost identical: 0.04 % compliance difference
Speedup drops to 5×: density-filter work still runs on the fine mesh
OC plus density filter never meets the design-change tolerance
Stopped instead on a compliance plateau
Structural Optimization (B-KUL-H0T88A)
9
Notes: PRESENTER: Tiebert | Target ~50 s
Step 3 repeats the comparison with a density filter instead of a sensitivity filter. The designs are again almost identical, 0.04 percent in compliance.
But the speedup drops from 21 to about 5. The reason: the density filter adds a chain-rule convolution and a volume check that still run on the full 600 by 200 density mesh, so they do not shrink with the analysis mesh.
One more observation: with a density filter the OC update never quite meets the design-change tolerance - it oscillates at the boundary - so we stop it on a compliance plateau instead.

## Slide 10: Step 4: MMA and Heaviside projection
OC update replaced by the method of moving asymptotes (MMA)
MMA alone: design close to OC; density-filter convergence issue remains
Heaviside projection pushes the design towards black-and-white
Near-binary layout: ~17 % lower compliance than the gray design
All three thresholds agree within 0.7 %; 0.5 is best
η = 0.3
η = 0.5 (best)
η = 0.7
Structural Optimization (B-KUL-H0T88A)
10
Notes: PRESENTER: Tiebert | Target ~65 s
Step 4 swaps the optimality-criteria update for MMA, the method of moving asymptotes. MMA on its own gives a design close to the OC result, and it does not by itself fix the density-filter convergence issue from the previous slide.
The real benefit comes with Heaviside projection, which pushes the gray material towards either solid or void. On the right are the three projected designs, for thresholds 0.3, 0.5 and 0.7: all near black-and-white, all the same load path.
The projected compliance is about 17 percent below the gray density-filtered design. The three thresholds differ by less than 0.7 percent; 0.5 is marginally the best.

## Slide 11: Where does the speedup come from?
Classical OC: 82 % of the time is the finite element solve
MTOP shrinks that solve by about 40×
Filtering, assembly and the optimizer still act on the full density mesh, so they cap the speedup
MMA runs become dominated by the optimizer subproblem
Structural Optimization (B-KUL-H0T88A)
11
Notes: PRESENTER: Tiebert | Target ~50 s
So where does the speedup actually come from? This chart breaks each run into algorithmic phases.
For the classical OC run, the green block - the finite element solve - is 82 percent of the time. MTOP shrinks exactly that block: the coarse solve is about 40 times faster.
What it cannot shrink is the rest - the filtering, the assembly, the optimizer - which still act on the fine density mesh. That is why the total speedup is 21 and not 40. For the MMA runs the red optimizer block dominates, so there the equilibrium solve is no longer the bottleneck.

## Slide 12: What MTOP really buys you
A plain coarse model reaches within 0.6 % of the fine design
For this 2D case with a large filter, a coarse model already captures the load path
But that coarse design is grayer and fixed at the coarse resolution
MTOP keeps the full 600 × 200 design while paying only the coarse solve
Coarse-resolution baseline: 120 × 40 analysis = density mesh
Structural Optimization (B-KUL-H0T88A)
12
Notes: PRESENTER: Tiebert | Target ~50 s
One honest qualification. We also ran a plain coarse model, 120 by 40 for both the analysis and the design. Re-analyzed on the fine mesh, it lands within 0.6 percent of the full design.
So for this 2D beam, with a fairly large filter, even a crude model already finds the load path. The difference is that this coarse design is locked to 120-by-40 resolution and is noticeably grayer.
MTOP's real value is that it keeps the full 600-by-200 design description while only paying for the coarse solve.

## Slide 13: Conclusions
MTOP reproduces the classical MBB design to within 0.05 % compliance
Sensitivity filtering: 21× faster; density filtering: 5× faster
The speedup comes from the cheaper coarse equilibrium solve
OC plus density filtering converges only in the compliance sense
Heaviside projection gives the lowest, near-binary compliance (threshold 0.5)
Structural Optimization (B-KUL-H0T88A)
13
Notes: PRESENTER: Tiebert | Target ~40 s
To conclude. MTOP reproduces the classical MBB design to within 0.05 percent compliance. It is 21 times faster with sensitivity filtering and 5 times faster with density filtering.
The speedup comes from the cheaper coarse equilibrium solve, and is capped by the operations that still run on the fine mesh. OC with density filtering converges only in the compliance sense. And Heaviside projection gives the lowest, near-binary compliance, best at threshold 0.5.
The chart summarizes all nine runs - cost on the left, compliance on the right.

## Slide 14: Future work and outlook
Where MTOP pays off most
  3D problems: the equilibrium solve dominates far more, so the speedup is larger
  Smaller filter radii and finer features, which a plain coarse model cannot resolve
  Cases that need the fine design description, not only the overall load path
Open issues and limitations
  Density filtering needs a convergence criterion beyond the design-change tolerance
  Filtering, assembly and the optimizer still scale with the fine mesh and cap the speedup
  With MMA the optimizer subproblem, not the FE solve, is the bottleneck
Thank you for your attention. Questions?
Structural Optimization (B-KUL-H0T88A)
14
Notes: PRESENTER: Tiebert | Target ~30 s
To close, a brief outlook. Our headline numbers are for a 2D beam, where a plain coarse model already came within 0.6 percent, so the 2D benefit was modest. MTOP pays off most where the equilibrium solve genuinely dominates the cost: in 3D, with much larger systems, and where the design has fine features a coarse model cannot resolve, so keeping the fine density description is worth it.
Three open issues from this study: density filtering needs a better convergence criterion than the design-change tolerance; the filtering, assembly and optimizer steps still scale with the fine mesh and cap the speedup below the 40 times of the solve itself; and with MMA the optimizer subproblem, not the FE solve, becomes the bottleneck.
Thank you - we are happy to take questions.